Part 1: Basics

10 Different Protocols
- HTTP -Hyper Text Transfer Protocol
- TCP
- UDP
- ARP (Address Resolution Protocol)
- SSDP (Simple Service Delivery Protocol)
- LLMNR (Link-Local Multicast Name Resolution)
- DNS	(Domain Name Service)
- ICMPv6 (Internet Control Message Protocol)
- DHCPv6 (Dynamic Host Configuration Protocol)
- LLDP	(Link Layer Discovery Protocol)

2.
www.google.co.in

If we look at the frame section of the GET request we see that the time the packet arrived
is 16:46:06.652928000 IST

ScreenShot1

The same section for the HTTP OK shows an arrival time of
16:46:06.815843000 IST

ScreenShot2

The difference of these two times gives:
.815843000 - .652928000 = .162915000 seconds
3.
We cannot get the Internet Address of www.google.com from here due to Proxy Server.
All packets go to 202.141.80.22 from our machine and then to the appropriate destination. Similarly all the packets we receive come first to the proxy server 202.141.80.22 and then to our machine.
Hence for our all packets seem to come from the proxy server.

Part 2 : Ethernet

GET → 51
HTTP:// OK → 88

For the Ethernet Frame containing HTTP GET MESSAGE

1. 48-bit Address of Machine → 38:60:77:c3:49:59 (IP Address- 172.16.27.28)
2. The destination address in the Ethernet frame is 00:24:f9:9d:70:00
  No, This is not the Ethernet address of the website with the RFC.
  It is the address of the router the host computer is directly connected to (default gateway), which is the link used to get off the subnet. This can be verified by using “ arp -n “ option.
  The default gateway is IP Address 172.16.24.254 → Hardware Address 00:24:f9:9d:70:00
3. The hex value for the Frame Type field is 0x0800
  0x0800 stands for Internetworking Prorocol (IP)
Type field (bytes 13-14), which lists a number that identifies the protocol of the Data contained	in the frame
For reference, the types of values this field could be are the following:
  1. 0 – 1500 length field (IEEE 802.3 and/or 802.2)
  2. 0×0800 IP(v4), Internet Protocol version 4
  3. 0×0806 ARP, Address Resolution Protocol
  4. 0×8137 IPX, Internet Packet eXchange (Novell)
  5. 0x86dd IPv6, Internet Protocol version
1. ScreenShot
  AS can be seen from the screenshot ASCII “G” appears 66 bytes from the start of the Ethernet Frame.
              ----------------
For HTTP RESPONSE (OK) MESSAGE

1. The value of the Ethernet source address is 00:24:f9:9d:70:00.
   This is neither the address of my computer nor of the destination website with the RFC.
   It is the Ethernet address of the router (Default Gateway)or switch that the local computer is connected to.

   Already checked with “arp -n”
   The default gateway is IP Address 172.16.24.254 → Hardware Address 00:24:f9:9d:70:00
2. The destination address in the Ethernet frame is the MAC address (Ethernet Address) for my network card, which is 38:60:77:c3:49:59 (IP Address – 172.16.27.28)
3. The hex value for the Frame Type field is 0x0800
  0x0800 stands for Internetworking Prorocol (IP)
  Rest of the information is same as answer in question 3 above.

Part 3 : IP

IP Address of my Computer – 172.16.27.28

Within the header, the Value in the Upper Layer Protocol Field is UDP ( 0x11) i.e. 17.

IP header length = 20 bytes
Bytes in the payload of IP header = 36 bytes
Bytes in Payload = Total length – Length of Header = 56 -20 = 36 bytes

The IP Datagram has not been fragmented
Here the Flags value is 0x00
The more fragments bit =0 which means it is the last fragment.
The fragment offset = 0
which tells us that it is not fragmented.
//Description of flag:
Flags:
A 3 bit field is used which says if the datagram is a fragmented data frame or not.
Bit 0: reserved, must be zero
Bit 1: (AF) 0 = May Fragment, 1 = Don't Fragment.
Bit 2: (AF) 0 = Last Fragment, 1 = More Fragments.

The fields that always change are:
Identification , Header Checksum

The fields that stay constant across the IP datagrams are:
- Version (since we are using IPv4 for all packets)
- Header Length (which is 20 bytes)

Identification Field Value : 0x18c4 (6340)
TTL Field Value : 255
Identification Number changes for all the ICMP TTL-exceeded replies.
The TTL values remain unchanged i.e 255 for all the ICMP TTL-exceeded replies.

The Identification Number changes because it is a unique number for each of the